## Slide 1
Introduction to Solid Mechanics
Displacements and deformation
Strains and rotations

## Slide 2
Displacements and deformations
Material and Spatial descriptions
X – undeformed configuration
x – deformed configuration
X = X(x,t) = χ-1(x,t)
x = χ(X,t)
Motion described in terms of X
Motion described in terms of x
Notes: Big difference is in the material frame we care about the mapping –chi. We need to know where the particle came from since it is tagged. In the spatial frame, we have no idea where things came from, just that it is now there.

## Slide 3
Displacements and deformations
Displacement field
Lagrangian – GPS, levelling, weather balloons, device moves with the medium
Eulerian – pitot tubes, air temp, OBP, common in fluid mechanics (maybe InSAR)
Notes: Discuss steady fluid flow through a constricting pipe – the time derivative of velocity is 0 (spatially steady field), however the fluid particles itself experience a change in velocity from the open channel to the convergent zone

## Slide 4
Displacements and deformations
In typical geophysical studies, displacements are small such that the material and spatial descriptions are nearly identical. But in geodynamics, where we simulate large deformations and changing configurations, this distinction is important.
advection
When we calculate the material derivative of some quantity that is being advected, we get -
Time derivative for a particle
(using spatial description – x, not X)
Notes: Motivate why they should care about this – landslides, glaciers, any flow problems

## Slide 5
Differing derivatives based on coordinate system

## Slide 6
Differing derivatives based on coordinate system

## Slide 7
Deformations, Strains and Rotations
Deformation gradient (for coordinates)
Displacement gradient
What does it mean when F = I?

## Slide 8
Deformations, Strains and Rotations
Strain tensors
Deformation gradient (for coordinates)

## Slide 9
Deformations, Strains and Rotations
Displacement field and its gradient
Displacement gradient
Infinitesimal deformation

## Slide 10
Deformations, Strains and Rotations
Infinitesimal Strain tensor
For a 3 component displacement field, write out all components of the strain tensor

## Slide 11
Deformations, Strains and Rotations
Rotation tensor (again)
strain tensor (symmetric)
rotation tensor
(skew-symmetric)
For a 3 component displacement field, write out all components of the rotation tensor. Can you represent this as a cross product?

## Slide 12
Deformations, Strains and Rotations
For a 3 component displacement field, write out all components of the rotation tensor. Can you represent this as a cross product?

## Slide 13
Decomposing the displacement gradient

## Slide 14
Compatibility conditions
For a 3 component displacement field, we can easily compute its spatial derivatives => strains and rotations. But does it work vice versa?

## Slide 15
Compatibility conditions
For 6 independent strain components, there are 9 strain-displacement equations. How to solve?
This guarantees that the strains can be integrated to give a single-valued u, but it does not guarantee a unique u. Why?
Notes: These 6 equations are interlinked, actually there are only 3 independent equations

## Slide 16
Displacements from strains
Given a strain tensor (symmetric), first verify if it indeed represents a compatible strain tensor and then integrate it to compute displacements analytically (and numerically)
  1-d problem, 0 < x < 5: εxx = log(x), compute ux
  2-d problem, 0 < x < 1, 0 < y < 1: exx,eyy,ezz,exy = 0, ezx = x/(x2 + y2)
  ezy = y/(x2 + y2), compute uz
  2-d problem, 0 < x < 1, 0 < y < 1: ezz , ezx , ezy = 0,
  exx = ((k+1)x2y + (k-3)y3)/(x2 + y2)2
    eyy = ((k-3)x2y + (k+1)y3) /(x2 + y2)2
    exy = (4xy2)/(x2 + y2)2, compute ux and uy (for k = 4)

## Slide 17
Principal Strains
The strain tensor can be rotated such that all the off-diagonal components vanish and we are left only with diagonal terms – principal strains

## Slide 18
Principal Strains
The strain tensor can be rotated such that all the off-diagonal components vanish and we are left only with diagonal terms – principal strains

## Slide 19
Principal Strains
The strain tensor can be rotated such that all the off-diagonal components vanish and we are left only with diagonal terms – principal strains

## Slide 20
Principal Strains
Find the rotation angle that makes shear strain 0 and then what are the other components?
2
2
What is the maximum shear strain for this system?

## Slide 21
Strain invariants

## Slide 22
Assignments
From the horizontal displacement field given to you, first plot the displacement vectors on the elevation grid.
Project the displacements on to the elevation gradient direction (unit vector) – to do this you will have to resample either the displacements or the elevation data. Discuss what this quantity means?
Estimate the total change in GPE due to materials moving. Hint: to do this you will have to interpolate the displacements and compute the 2-d integral of down-slope mass transport.
Calculate the horizontal strain components from the displacement field
Plot the trace of the strain tensor and overlay it with displacement field. What does the trace represent?
Bonus: plot the principal strains at each point (maybe not each point because that will look overcrowded)